UNIVERSITY OF CAMBRIDGE

Department of Geography

CHEMICAL HAZARD RISK ASSESSMENT FORM

Completing this document fulfils the requirements of the COSHH and DSEAR Regulations relating to a written risk assessment

Experiment or Procedure (include a brief description & reaction conditions i.e. temperature, solvent, work up procedures and frequency of exposure): PREPARATION OF SOIL, SEDIMENT OR OTHER MATERIAL FOR POLLEN AND DINOFLAGELLATE CYST ANALYSIS Samples are treated with a series of hot (~90(C) or cold acids (including hydrofluoric acid [HF]), alkalis and organic solvents to remove organic and inorganic fractions, leaving residues which contain fossil pollen and/or dinoflagellate cysts Each room being used by one person each working day to prepare batches of up to 20 samples.” The Preparation Rooms are equipped with pure water machines, ovens, centrifuges and specially designed acid digestion fume cupboards, in which the majority of the procedure is executed

Risks associated with the procedure (What are the hazards and risks?): The main hazards are associated with handling acids (including hydrofluoric acid), alkalis and organic solvents during the procedure. The main risks involved are the inhalation and ingestion of, or contamination by, these reagents. An additional minor hazard is the use of a Bunsen burner to ‘flame’ sieves. The risk here is of physical injury (burns), and as a source of ignition.

Risk implications: Is there any substance used or formed that might give rise to explosion (e.g. flammable gases/liquids)? YES If yes, how can you ensure that no explosion occurs? FLAMMABLE LIQUIDS ARE STORED & USED AWAY FROM SOURCES OF IGNITION, USUALLY IN THE FUME CUPBOARD. Is it reasonably foreseeable that the lower explosive limit will be reached in the event of a leak/spillage? NO If yes, a more detailed risk assessment is required. Is there likelihood of copious amounts of gas being released or thermal runaway? NO Can any of the substances be substituted for a less hazardous substance? NO What could happen if there was catastrophic failure of the apparatus? FAILURE OF THE FUME CUPBOARD COULD RESULT IN HYDROFLUORIC ACID FUMES ESCAPING INTO THE PREPARATION ROOM. In the event of an accident, who might be exposed? THE WORKER BOOKED INTO THE PREPARATION ROOM IS MOST AT RISK.

| Substances to be used (List ALL substances including solvents, expected products and by-products): |
| --- |
| Substances Used | Approx. Quantity | Physical Form i.e. dust, vapour, volatile liquid etc | Hazards i.e. flammable, corrosive, irritant, readily absorbed through skin | Exposure Route i.e. skin, eyes |
| Absolute alcohol | 2.5L | liquid | flammable, | Inhalation, Ingestion, Skin contact, eyes |
| Acetic acid 99% | 2.5L | liquid | flammable, corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Acetic anhydride 97% | 2.5L | liquid | flammable, corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Acetone (propanone) | 2.5L | liquid | flammable, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Decon 90 detergent | 5L | liquid | corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Hydrochloric acid conc. 35% | 2.5L | liquid | strong acid, corrosive, irritant | Inhalation, Ingestion, Skin contact, eyes |
| Hydrochloric acid 7% | 5L | liquid | corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Hydrofluoric acid conc. 48% | 2L | liquid | strong acid, corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Methylated spirit | 5L | liquid | flammable, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Nitric acid conc. 1.42 spg | 2.5L | liquid | Strong acid, corrosive, irritant, | Inhalation |
| Nitric acid 10% | 5L | liquid | corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Potassium hydroxide pellets | 2.5Kg | solid | strong alkali corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Potassium hydroxide 10% solution | 5L | liquid | strong alkali corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Sodium hydroxide pellets | 2.5Kg | solid | strong alkali corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Sodium hydroxide 10% solution | 5L | liquid | strong alkali corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Sodium pyrophosphate 4.4% soln. | 5L | liquid | irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Sulphuric acid conc. 98% | 2.5L | liquid | strong alkali corrosive, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Tertiary butyl alcohol | 2.5L | liquid | flammable, irritant, | Inhalation, Ingestion, Skin contact, eyes |
| Sodium Carbonate | 1kilo | Powder | Irritant, flammable | Inhalation, Ingestion, Skin contact, eyes |

| Are any of the substances listed above R42, R43, R45, R46, R49, R60, R61, R64? NO (If yes, contact Occupational Health and refer where necessary to the University Code of Practice on the Safe Use of Carcinogens etc) |
| --- |
| Control measures to be used (continue on a separate sheet if necessary): |
| Containment: | Personal Protective Equipment: |
| Fume cupboard YES | Lab coat / overalls YES |
| Glove box / isolator NO | Chemical apron YES |
| Safety cabinet YES | Gloves YES |
| Local exhaust ventilation YES | Eye Protection YES |
| Other (specify) | Respiratory protective equipment NO |
|  | Other (specify) FULL FACE VISOR |
| Are any additional controls required? (Consider nearby sources of ignition, formation of explosive atmospheres/mixtures, asphyxiation in confined spaces) Lab coat, gloves and eye protection are the minimum required personal protection for all reagent use. In addition, nitrile gloves and a protective apron are required for handling concentrated acids. Hydrofluoric acid use requires heavy-duty rubber gloves, a face mask, a rubber apron and a beaker of saturated sodium carbonate solution. |
| Disposal measures to be used during and after the procedure: (Also consider by-products and washings) All reagents to be disposed of via the fume cupboard sink which is connected to a sump filled by marble chips. This neutralises all acidic waste products. |
| Emergency Procedures (emphasise any special hazards): |
| Shutdown Procedures: In an emergency, close the fume cupboard sash fully, vacate the preparation room and summon help. |
| Action in the event of fire (type of fire extinguisher): POWDER |
| Action in the event of spillage or uncontrolled release: don’t panic. Small spills in the fume cupboard can be safely contained with saturated sodium carbonate solution. Larger spills outside the fume cupboard may be controlled with a spill containment pack and/or slaked lime. If in doubt, vacate the preparation room and summon help. If fume escape or inhalation is suspected, vacate the preparation room and summon help. |
| Emergency treatment for personnel in the event of contamination, exposure to fumes or other adverse effects Eyes: Irrigate with cool clean water for at least 20 minutes, summon first aid, send to A & E Unit at Addenbrookes Hospital. Skin: Remove contaminated clothing and flood skin with cool clean water and summon first aid. If HF suspected, apply calcium gluconate gel to the affected area continuously for 15 minutes, bandage affected area with dressing soaked in gel and send to the A & E Unit at Addenbrookes Hospital. Inhalation: Remove casualty to fresh air, summon first aid and send to A & E Unit at Addenbrookes Hospital. |
| Name of assessor: |  |
| Signature: | Date: |
| Name of co-signatory: |
| Signature: | Date: |

Note:	This risk assessment should be reviewed at least annually and when there is any significant change in procedure.